Date & Time: 01/30/2013
Location: Campus
Computing context: Macho Mac

Continuing from last time:
- Fixing the G2J problem is not optional.
- Checking out the indexing in Helena's lookup and bilinear interpolation routines.
- Peter's code does something like a *tri*-linear interpolation: between chemical compositions, temperature, and pressure.
- In Peter's eos tables, the log(rho) values are specified to 6 significant digits.
- Making a new rho lookup table for Helena (rho_test_3.txt) where the P, T, and rho are all set to their log values. (Before, table had logP, logT, linear rho). Let's see if that makes any difference.
  - Got better agreement b/w the codes (like, not off by factors of 2 or 3 anymore) with rho_test_5.txt. This one had logP, logT, and logRho values. The resolution of the (Helena) table is the same as the eostable Peter's code is using, though it extends over a larger, uniform T/P range.
  - The rho values Peter's code returns are slightly larger than the ones Helena returns. This might be a resolution issue.
  - To test, I'm going to decrease the resolution on the Helena table (make dT and dP bigger), and check to see how the results change. This courser resolution table is rho_test_6.txt
    - It makes a slight difference, but let's test it w/ even more extreme resolution differences.
  - Make dP and dT smaller this time. (rho_test_7.txt)
    - Increasing the table resolution by a factor of 10 (both in logT and logP) *does* seem to get the rho lookup values to agree (at least, to the print-out precision rounding limit for the fortran write(6,*) statements I'm using).
Next steps:
- See if I can figure out why calling invstate returns different logRho values than calling eostab does...
- Check whether this precision level gets the rest of the lookup values (cP, delta, etc) to agree b/w the codes.
  - Try to figure out precisely why Helena doesn't return identical rho-values when I use a lookup table w/ the same precision and inputs as in Peter's code.
    - This probably has to do w/ the print-out precision his code is using/putting into the Helena lookup table. (I.e., writing out higher precision values than it should).
    - Figure out how to specify the print-out format to only do a certain number of sig figs, and see whether using a lookup table based on those values can get Peter and Helena to agree on logRho values for identical T/dT P/dP ranges and values.
- If all the lookup values agree w/ the higher-resolution tables, run each code and plot the resulting densities at each mass cell against each other.
- If those agree, then compare the G2J values from the two runs against each other and see whether that issue caused by the slight density differences has been fixed.

Today's work:
- See if I can figure out why calling invstate returns different logRho values than calling eostab does.
  - The XX and YY values equal 0 when I call eostab from within invstate, but not when I call eostab directly from main.
    - In other words, invstate is returning eos value for an object made entirely of heavy elements. This explains why invstate is returning higher densities than eostab (directly) does.
    - Got invstate and eostab to use the same X and Y abundances, through bizarre trial-and-error variable name/scoping process. I don't understand exactly why the current configuration does the trick, but now it works. (See the git-commit of eostableKludge.f from today's date if you need to remind yourself of what that ended up looking like, code-wise.)

- Check whether the current (high) lookup table P/T resolution level gets the rest of the lookup values (cP, delta, etc) to agree b/w the codes.
  - Remove the debugging print statements from the fortran code, and recompile